## Slide 1: Enhancements of Phase 5 to Support Water Resource Planning in the Potomac River Basin
May 11, 2010
Cherie Schultz, Sarah Ahmed, Heidi Moltz, Sunghee Kim, Ross Mandel
Interstate Commission on the Potomac River Basin

## Slide 2: Enhancements of Phase 5 to Support Water Resources Planning
Objective: enhance simulation of flows – with focus on low flows (drought flows)
Motivation
  Sustainable flows project (ICPRB/TNC/USACE)
  Impact of climate change on Washington, DC, metro area water supply (ICPRB – CO-OP) (working with USGS/CBP)
ICPRB enhancements
  I. Implementation of nonlinear groundwater storage/discharge algorithm in hydro model
  II. Model re-segmentation for representation of additional dams/impoundments in Potomac basin

## Slide 3: Related Efforts/Other Potential Uses
VADEQ developing water resource management/water supply planning tool based on Phase 5 hydro
USGS/CBP assessing impact of climate change on flows
Potential future use of hydro model in flow TMDLs?

## Slide 4: I. Nonlinear Groundwater Storage/Discharge Algorithm
Phase 5 calibration provides good match to range of observed flows
  High flows – deliver majority of loads
  Low flows – of interest in some TMDLs & to water supply planners
HSPF’s linear groundwater storage/discharge algorithm causes some under-simulation of low flows
Implementation of nonlinear storage/discharge algorithm helps attenuate falloff of flows during dry periods

## Slide 5
Chart: Potomac River at Hancock (PU6_3610_3530)

## Slide 6
Chart: Shenandoah River at Millville (PS5_4380_4370)

## Slide 7: HSPF Groundwater Component
QGW
S
Each river segment associated with a single groundwater reservoir with storage, S
Groundwater discharge, QGW, dominates simulated flows during dry periods
HSPF assumes simple “linear” relationship: QGW  S

## Slide 8: Linear Groundwater Recession Algorithm
Water balance
during dry periods:
dS/dt = - QGW
Linear
storage/discharge
relationship:
S = k QGW
Q(t0)
t0
t 
Q(t) = Q(t0) e –k (t – t0)

## Slide 9: Limitations of Simple Linear Model
Attenuation of flows often too rapid during dry periods
Areas with carbonate rock geology are particularly challenging
Chart: Shenandoah River at Millville

## Slide 10: Alternative Approaches in Watershed Models
HSPF’s existing nonlinear groundwater algorithm (parameter KVARY) – hasn’t proved useful in Phase 5 calibration
Nonlinear groundwater storage/discharge model
  ICPRB implementation in Phase 5.2’s HSPF
  ICPRB/UMD implementation in Potomac SWAT (with Prof. Kaye Brubaker)
Others? – keep searching literature

## Slide 11: Nonlinear Groundwater Storage/Discharge Model
Long history in hydrology literature
  Brutsaert and Nieber, 1977
  Some other refs
  Renewed interest in recent years
Physical basis - from 1-d Boussinesq equation – describing transient ground water table of varying thickness above a impermeable layer, with Dupuit assumption.
2 parameter model – potential for improving simulation of drought flows

## Slide 12: Comparison of Linear & Nonlinear Storage/Discharge Models
 | Linear model | Nonlinear model
Water balance |  | 
Storage-discharge relationship | Q = k S | Q = k S
Solution for Q |  | 
Solution for S |  | 
Q = groundwater discharge
S = groundwater storage

## Slide 13: Plots of Discharge vs. Time
Chart: Days
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40 | 41 | 42 | 43 | 44 | 45 | 46 | 47 | 48 | 49 | 50 | 51 | 52 | 53 | 54
linear (k=0.05) | 100 | 95.1229 | 90.4837 | 86.0708 | 81.8731 | 77.8801 | 74.0818 | 70.4688 | 67.032 | 63.7628 | 60.6531 | 57.695 | 54.8812 | 52.2046 | 49.6585 | 47.2367 | 44.9329 | 42.7415 | 40.657 | 38.6741 | 36.7879 | 34.9938 | 33.2871 | 31.6637 | 30.1194 | 28.6505 | 27.2532 | 25.924 | 24.6597 | 23.457 | 22.313 | 21.2248 | 20.1897 | 19.205 | 18.2684 | 17.3774 | 16.5299 | 15.7237 | 14.9569 | 14.2274 | 13.5335 | 12.8735 | 12.2456 | 11.6484 | 11.0803 | 10.5399 | 10.0259 | 9.5369 | 9.0718 | 8.6294 | 8.2085 | 7.8082 | 7.4274 | 7.0651 | 6.7206
nonlinear (beta=1.5) | 100 | 93.3487 | 87.2744 | 81.7159 | 76.6196 | 71.9384 | 67.631 | 63.6606 | 59.9951 | 56.6056 | 53.4668 | 50.5557 | 47.8523 | 45.3382 | 42.9971 | 40.8146 | 38.7772 | 36.8733 | 35.0919 | 33.4235 | 31.8592 | 30.3911 | 29.0117 | 27.7146 | 26.4937 | 25.3434 | 24.2588 | 23.2352 | 22.2684 | 21.3545 | 20.4899 | 19.6714 | 18.8958 | 18.1606 | 17.463 | 16.8006 | 16.1714 | 15.5731 | 15.0041 | 14.4624 | 13.9465 | 13.4548 | 12.986 | 12.5387 | 12.1117 | 11.7039 | 11.3142 | 10.9416 | 10.5851 | 10.244 | 9.9174 | 9.6046 | 9.3047 | 9.0172 | 8.7415
nonlinear (beta=4) | 100 | 90.7574 | 82.9126 | 76.1821 | 70.3528 | 65.2616 | 60.782 | 56.8141 | 53.2783 | 50.1104 | 47.258 | 44.6781 | 42.335 | 40.1988 | 38.2443 | 36.4503 | 34.7986 | 33.2735 | 31.8616 | 30.5514 | 29.3326 | 28.1965 | 27.1351 | 26.1418 | 25.2104 | 24.3356 | 23.5125 | 22.737 | 22.0051 | 21.3135 | 20.659 | 20.0389 | 19.4507 | 18.8921 | 18.3609 | 17.8553 | 17.3736 | 16.9142 | 16.4756 | 16.0566 | 15.6558 | 15.2723 | 14.9049 | 14.5526 | 14.2147 | 13.8903 | 13.5786 | 13.279 | 12.9907 | 12.7133 | 12.446 | 12.1884 | 11.94 | 11.7003 | 11.4689

## Slide 14: Results – Shenandoah River at Millville
Chart: 

## Slide 15: FDC Results – Shenandoah River at Millville
Chart: Flow (cfs)

## Slide 16: Results – Potomac River at Hancock
Chart: 

## Slide 17: FDC Results – Potomac River at Hancock
Chart: Flow (cfs)

## Slide 18: II. Model Re-segmentation in Potomac Basin

## Slide 19: Summary
Nonlinear groundwater storage/discharge model
  Leads to improvement in simulatation of drought flows
  Causes some deterioration in simulation of mid-flows
  Results in improvement in over-all measure of model agreement with observed flows - Nash-Sutcliffe efficiencies
Re-segmentation of Potomac Basin